## Slide 1: NCAP: Network-Driven Packet Context-Aware Power Management for Client-Server Architecture
Mohammad Alian, Ahmed Abulila, Lokesh Jindal, Daehoon Kim, Nam Sung Kim
Electrical & Computer Engineering
University of Illinois Urbana-Champaign

## Slide 2: Executive Summary
problem: servers running on-line data-intensive (OLDI) applications (e.g., web serving) are often underutilized
  energy is wasted at low- to medium-load levels
solution? power management
challenge: conventional power management polices fail to satisfy SLA (deadline for processing a request)
  poor low-power state governors
  overhead of transitioning b/w power states
NCAP: aggressive processor power management based on context of network packet through a network interface card (NIC)
  37-69% lower processor energy consumption than a baseline server while satisfying SLA

## Slide 3: Outline
motivation
  power management challenges in servers running OLDI-applications
methodology
  dist-gem5 –full-system/cycle-accurate simulator for distributed computer systems
background
  client-server architecture
  conventional power management
network-driven, packet context-aware, power management
  HW/SW joint approach augmenting conventional power management techniques
evaluation
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 4: Motivation
online data intensive (OLDI) services
  e.g., key-value stores, web-serving
  client-server architecture
  obligated to satisfy SLA (Service Level Agreement)
load on an OLDI server dynamically changes
  unpredictable load in short time periods
  load imbalance amongst servers in a data-center
OLDI server energy consumption
  servers – energy-inefficient at low- to medium-load levels
  causes SLA violation for OLDI services due to slow power state transitioning
Chart: Server Power Distribution [1]
| CPUs | DRAM | Disks | Others | Cooling
Sales | 42 | 11.7 | 14.3 | 16.6 | 15.4
methodology
background
NCAP
evaluation
conclusion
motivation
[1] L. A. Barroso, et al. “The Datacenter as a Computer” Second Edition, 2013

## Slide 5: Methodology
run two representative OLDI applications
  Memcached and ApacheBench
model a multi-node computer cluster using dist-gem5
  one server and several clients at various load levels
category | configuration
O3 core | 4 cores, each w/ 15 P states (0.65V/0.8GHz to 1.2V/3.1GHz) & 3 C states (C1, C3, & C6)
network | 10Gbps Intel GbE NIC and switch w/ 1 μs
OS | Linux Ubuntu 11.04 (kernel version 2.6)
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 6: dist-gem5
parallel/distributed gem5 for simulating distributed computer systems
each node is a full-system model
  operating system + processor + memory + IO
network switch process
  model an arbitrary network topology, speed, latency
dist-gem5 available @ gem5.org
  unified infrastructure for evaluating distributed systems
  enable researches cutting across operating system,
  processor/memory architecture, and network
    heterogeneous datacenters
    performance/power studies of networked systems
    big-data architecture, …
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 7: Client-Server Architecture
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 8: Client-Server Architecture
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 9: Client-Server Architecture
receive a packet encapsulating a request
process packet
PKT
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 10: Client-Server Architecture
receive a packet encapsulating a request
process packet
process request
send response
REQ
RES
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 11: Client-Server Architecture
receive a packet encapsulating a request
process packet
process request
send response
Takes ~80µs on average
REQ
RES
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 12: Client-Server Architecture
receive a packet encapsulating a request
process packet
process request
send response
REQ
RES
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 13: Processor Power Management
performance (active P) state: P0 to Pn w/ f(Pn-1) > f(Pn)
  performace and powersave
    running cores at P0 and Pn
  ondemand
    periodically sampling core utilization and adjusting P-state proportionally
power (or idle C) state: C0 (idle), C1 (halt), C3 (sleep), C6 (off)
  menu
    transition cores to different C states based on the transition history
  ladder
    gradually transition cores to deep C states
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 14: Processor Power Management
HW/SW overheads for changing P and C states
  HW overhead of 5 to 60 μs in intel i7-3770
  governor invocation overhead
    minimum invocation period of ondemand in Linux is hard coded to 10ms
methodology
background
NCAP
evaluation
conclusion
motivation
Chart: Ondemand Invocation Period (ms)
| 1 | 10 | 20 | 40
HIGH | 1.1404 | 0.90573 | 0.79056 | 1
MED | 0.87618 | 0.79201 | 0.8995 | 1
LOW | 0.69777 | 0.70985 | 0.88302 | 1
Apache running at different load levels

## Slide 15: Conventional Power Management
 | transition to Idle? | V/F level
 | no | highest
 | no | dynamic (ondemand)
 | yes (menu) | highest
 | yes (menu) | dynamic (ondemand)
OLDI applications at med-load level
  A: Apache M: Memcached
power management policies
SLA Violation
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 16: ondemand Governor
correlation b/w BW(Rx/Tx) and U(core) (i.e., F(core))
  BW(Rx/Tx) as a proxy for U(core) changes
late reaction to high/low core utilization
  11ms and 7ms late frequency increase/decrease
BW(rx,tx) ~ U(core)
Chart: Time (s)
11ms
7ms
Apache w/ 10ms invocation period
for ondemand governor
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 17: menu Governor
Chart: Time (s)
TC1 | 0.029959 | 0.028638 | 0.042808 | 0.022613 | 0.052981 | 0.005607 | 0.039044 | 0.01256 | 0.023549 | 0.043223 | 0.034591 | 0.024192 | 0.087616 | 0.042983 | 0.043063 | 0.0034946 | 0.12131 | 0.04257 | 0.036752 | 0.04273 | 0.01828 | 0.092784 | 0.027335 | 0.022597 | 0.14725 | 0.03021 | 0.011085 | 0.018361 | 0.024977 | 0.031914 | 0.020082 | 0.042013 | 0.0158 | 0.019022 | 0.0001838 | 0.025622 | 0.62827 | 0.79348 | 1.6318 | 0.039208 | 0.63819 | 1.4846 | 0.030427 | 0.039441 | 0.038548 | 0.039392 | 0.037949 | 0.038802 | 0.012038 | 0.77797 | 0.77506 | 1.2182 | 0.97193 | 0.098442
ineffective in waking up cores in time
  unpredictable BW(Rx) surge
several short transitions during BW surge
  energy efficiency degradation
methodology
background
NCAP
evaluation
conclusion
motivation
Apache w/ ondemand
and menu governors

## Slide 18: Proposed NCAP P/C-State Governor
Desired P/C-state governor
react to change in core utilization in a timely manner
Approaches
predict changes in core utilization
  core utilization is highly correlated w/ network activity
hide P/C-state transition latency
  overlap P/C-state transition w/ packet reception
  and processing
methodology
background
NCAP
evaluation
conclusion
motivation
BW(rx)
U(core)

## Slide 19: NCAP Power Management – BW(Rx) Surge
High latency-critical request arrival rates detected w/ special HW in NIC
NIC will notify CPU by sending an interrupt to:
  activate cores
  boost frequency
  disable menu governor
R
R
R
Idle Active
Max Freq
Deep Idle
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 20: NCAP Power Management – BW(Rx) Surge
High latency-critical request arrival rates detected w/ special HW in NIC
NIC will notify CPU by sending an interrupt to:
  activate cores
  boost frequency
  disable menu governor
overlap P/C state transition time with packet reception and processing
Idle Active
Max Freq
Deep Idle
R
R
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 21: NCAP Power Management
Low latency-critical request arrival rates & low Tx interval are detected
i.e., processing for bursty requests is done
NIC will notify CPU by sending an interrupt to:
  reduce cores frequency
  enable menu governor
Idle Active
Max Freq
Deep Idle
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 22: NCAP Power Management
Low latency-critical request arrival rates & low Tx interval are detected
i.e., processing for bursty requests is done
NIC will notify CPU by sending an interrupt to:
  reduce cores frequency
  enable menu governor
R
Idle Active
Max Freq
Deep Idle
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 23: Effectiveness of NCAP – Frequency change
Apache
med-load level
top
  ondemand
  menu
bottom
  NCAP
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 24: Effectiveness of NCAP – Energy and Response Time
Chart: Norm. Time and Energy
| perf | ond | perf.idle | ond.idle | ncap | perf | ond | perf.idle | ond.idle | ncap | apache | memcached
Norm. 95th Resp. Time to SLA | 0.27868 | 0.79947 | 1 | 1 | 0.75714 | 0.57463 | 1 | 0.64837 | 1 | 0.74138
SLA violation | 0 | 0 | 0.060438 | 0.33162 | 0 | 0 | 0.92775 | 0 | 1.1418 | 0
Norm. Energy to "perf" | 1 | 0.79708 | 0.59677 | 0.55303 | 0.63364 | 1 | 0.83369 | 0.69652 | 0.54182 | 0.56035
Chart: Norm. Time and Energy
| perf | ond | perf.idle | ond.idle | ncap | perf | ond | perf.idle | ond.idle | ncap | apache | memcached
Norm. 95th Resp. Time to SLA | 0.17824 | 0.38717 | 0.61157 | 0.98739 | 0.44456 | 0.44146 | 0.80824 | 0.65035 | 1 | 0.70456
SLA violation | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.030301 | 0
Norm. Energy to "perf" | 1 | 0.77397 | 0.41336 | 0.39194 | 0.39403 | 1 | 0.53868 | 0.46141 | 0.3574 | 0.30314
95th response time
  normalized to SLA
energy consumption
  normalized to perf
config | Idle? | Freq level
perf | No | Highest
ond | No | ondemand
perf.idle | menu | Highest
ond.idle | menu | ondemand
ncap | NCAP | NCAP
methodology
background
NCAP
evaluation
conclusion
motivation
Med-Load
Low-Load

## Slide 25: Effectiveness of NCAP – Energy and Response Time
Chart: Norm. Time and Energy
| perf | ond | perf.idle | ond.idle | ncap | perf | ond | perf.idle | ond.idle | ncap | apache | memcached
Norm. 95th Resp. Time to SLA | 0.27868 | 0.79947 | 1 | 1 | 0.75714 | 0.57463 | 1 | 0.64837 | 1 | 0.74138
SLA violation | 0 | 0 | 0.060438 | 0.33162 | 0 | 0 | 0.92775 | 0 | 1.1418 | 0
Norm. Energy to "perf" | 1 | 0.79708 | 0.59677 | 0.55303 | 0.63364 | 1 | 0.83369 | 0.69652 | 0.54182 | 0.56035
Chart: Norm. Time and Energy
| perf | ond | perf.idle | ond.idle | ncap | perf | ond | perf.idle | ond.idle | ncap | apache | memcached
Norm. 95th Resp. Time to SLA | 0.17824 | 0.38717 | 0.61157 | 0.98739 | 0.44456 | 0.44146 | 0.80824 | 0.65035 | 1 | 0.70456
SLA violation | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.030301 | 0
Norm. Energy to "perf" | 1 | 0.77397 | 0.41336 | 0.39194 | 0.39403 | 1 | 0.53868 | 0.46141 | 0.3574 | 0.30314
95th response time
  normalized to SLA
energy consumption
  normalized to perf
config | Idle? | Freq level
perf | No | Highest
ond | No | ondemand
perf.idle | menu | Highest
ond.idle | menu | ondemand
ncap | NCAP | NCAP
methodology
background
NCAP
evaluation
conclusion
motivation
Med-Load
Low-Load
21%-49% lower energy
20%-35% lower energy

## Slide 26: Effectiveness of NCAP – Energy and Response Time
Chart: Norm. Time and Energy
| perf | ond | perf.idle | ond.idle | ncap | perf | ond | perf.idle | ond.idle | ncap | apache | memcached
Norm. 95th Resp. Time to SLA | 0.27868 | 0.79947 | 1 | 1 | 0.75714 | 0.57463 | 1 | 0.64837 | 1 | 0.74138
SLA violation | 0 | 0 | 0.060438 | 0.33162 | 0 | 0 | 0.92775 | 0 | 1.1418 | 0
Norm. Energy to "perf" | 1 | 0.79708 | 0.59677 | 0.55303 | 0.63364 | 1 | 0.83369 | 0.69652 | 0.54182 | 0.56035
Chart: Norm. Time and Energy
| perf | ond | perf.idle | ond.idle | ncap | perf | ond | perf.idle | ond.idle | ncap | apache | memcached
Norm. 95th Resp. Time to SLA | 0.17824 | 0.38717 | 0.61157 | 0.98739 | 0.44456 | 0.44146 | 0.80824 | 0.65035 | 1 | 0.70456
SLA violation | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.030301 | 0
Norm. Energy to "perf" | 1 | 0.77397 | 0.41336 | 0.39194 | 0.39403 | 1 | 0.53868 | 0.46141 | 0.3574 | 0.30314
95th response time
  normalized to SLA
energy consumption
  normalized to perf
config | Idle? | Freq level
perf | No | Highest
ond | No | ondemand
perf.idle | menu | Highest
ond.idle | menu | ondemand
ncap | NCAP | NCAP
methodology
background
NCAP
evaluation
conclusion
motivation
Med-Load
Low-Load
37%-69% lower energy

## Slide 27: Conclusion
conventional power management policies cannot react to the high processing demand of OLDI applications in a timely manner
  use of ondemand and/or menu governors – violation of SLA at unpredictable surge of requests
NCAP exploits the following to proactively make power management actions
  packet reception/processing delay in the network stack
  correlation between network traffic and core utilization
NCAP significantly reduces energy consumption at low to medium load levels w/o violating SLA
  37-69% lower processor energy consumption than a baseline server while satisfying SLA
methodology
background
NCAP
evaluation
conclusion
motivation

## Slide 28: Thank You