## Slide 1: NetDIMM: Low-Latency, Near-Memory Network Interface Architecture
Mohammad Alian, and Nam Sung Kim
Electrical and Computer Engineering
University of Illinois Urbana-Champaign

## Slide 2: Current Network Performance Trend in Datacenters
Higher and higher bandwidth
Chart: 
| 2010 | 2012 | 1014 | 2016 | 2018
1GE | 0.62 | 0.44 | 0.41 | 0.34 | 0.27 | 0.14 | 0.11 | 0.05 | 0 | 0
10GE | 1.17 | 1.46 | 1.68 | 1.82 | 1.74 | 1.6 | 1.4 | 1.21 | 1.01 | 0.8
40GE | 0 | 0 | 0.06 | 0.14 | 0.38 | 0.89 | 1.06 | 0.95 | 0.79 | 0.6
100GE | 0 | 0 | 0 | 0 | 0 | 0.15 | 0.49 | 1.02 | 1.59 | 2.09
1GE
10GE
40GE
100GE
*based on Infoneticsc forcasts

## Slide 3: Current Network Performance Trend in Datacenters
Higher and higher bandwidth
Innovations in network software stack to better utilize hardware
  Userspace networking (DPDK), software stack offloading (RDMA), etc.
Network latency approaches hardware limits
  ~2µ since the last decade!
Chart: 
| 2010 | 2012 | 1014 | 2016 | 2018
1GE | 0.62 | 0.44 | 0.41 | 0.34 | 0.27 | 0.14 | 0.11 | 0.05 | 0 | 0
10GE | 1.17 | 1.46 | 1.68 | 1.82 | 1.74 | 1.6 | 1.4 | 1.21 | 1.01 | 0.8
40GE | 0 | 0 | 0.06 | 0.14 | 0.38 | 0.89 | 1.06 | 0.95 | 0.79 | 0.6
100GE | 0 | 0 | 0 | 0 | 0 | 0.15 | 0.49 | 1.02 | 1.59 | 2.09
1GE
10GE
40GE
100GE
*based on Infoneticsc forcasts

## Slide 4: Current Network Performance Trend in Datacenters
Higher and higher bandwidth
Innovations in network software stack to better utilize hardware
  Userspace networking (DPDK), software stack offloading (RDMA), etc.
Network latency approaches hardware limits
  ~2µ since the last decade!
End to end hardware network latency?
  PCIe transactions contribute to up to 90% of
  network latency!
Chart: 
| 2010 | 2012 | 1014 | 2016 | 2018
1GE | 0.62 | 0.44 | 0.41 | 0.34 | 0.27 | 0.14 | 0.11 | 0.05 | 0 | 0
10GE | 1.17 | 1.46 | 1.68 | 1.82 | 1.74 | 1.6 | 1.4 | 1.21 | 1.01 | 0.8
40GE | 0 | 0 | 0.06 | 0.14 | 0.38 | 0.89 | 1.06 | 0.95 | 0.79 | 0.6
100GE | 0 | 0 | 0 | 0 | 0 | 0.15 | 0.49 | 1.02 | 1.59 | 2.09
1GE
10GE
40GE
100GE
*based on Infoneticsc forcasts
Chart: Packet Size (Bytes)
| 60 | 120 | 260 | 1500
PCIe Contribution | 0.91429 | 1.0286 | 1.0514 | 2.0571
NIC | 1 | 1.1429 | 1.2 | 2.6286
~77%
~90%
PCIe is the bottleneck in low-latency networking

## Slide 5: Executive Summary
We need: ultra low-latency networking in datacenters
  Emerging scale-out applications: short/critical message latency & tail latency at scale!
  Software-defined datacenters, memory disaggregation

## Slide 6: Executive Summary
We need: ultra low-latency networking in datacenters
  Emerging scale-out applications: short/critical message latency & tail latency at scale!
  Software-defined datacenters, memory disaggregation
💡Insight: What is the goal of networking?
  Inter-node memory copy
Picture taken from https://computing.llnl.gov/tutorials/parallel_comp/

## Slide 7: Executive Summary
We need: ultra low-latency networking in datacenters
  Emerging scale-out applications: short/critical message latency & tail latency at scale!
  Software-defined datacenters, memory disaggregation
💡Insight: What is the goal of networking?
  Inter-node memory copy
Network-attached Dual-Inline Memory Module (NetDIMM)
  ✅ Remove transactions over PCIe for network TX/RX
  ✅ Higher aggregate system memory bandwidth
  ✅ In-memory buffer cloning support

## Slide 8: Executive Summary
We need: ultra low-latency networking in datacenters
  Emerging scale-out applications: short/critical message latency & tail latency at scale!
  Software-defined datacenters, memory disaggregation
💡Insight: What is the goal of networking?
  Inter-node memory copy
Network-attached Dual-Inline Memory Module (NetDIMM)
  ✅ Remove transactions over PCIe for network TX/RX
  ✅ Higher aggregate system memory bandwidth
  ✅ In-memory buffer cloning support
Implementation & Performance: full-stack implementation on gem5
  50.7% & 30.9% lower netW latency & memory interference compared w/ PCIe NIC

## Slide 9: Outline
Introduction
Background
  DDR5 asynchronous memory operations
Network-attached DIMM
  NetDIMM hardware architecture
  NetDIMM software architecture
Evaluation
Conclusion

## Slide 10: Background: DDR5 Asynchronous Memory Access
Command bus
Data bus
Row Acc
Col Acc
data
DRAM Operation
tRCD + tCAS (deterministic)

## Slide 11: Background: DDR5 Asynchronous Memory Access
Command bus
Data bus
Row Acc
Col Acc
data
Command bus
Data bus
xRead
ADR
Resp bus
RDY
ID
Send
data
ID
⓵
⓶
⓷
⓸
DRAM Operation
tRCD + tCAS (deterministic)
Nondeterministic
NVDIMM-P Operation

## Slide 12: Background: DDR5 Asynchronous Memory Access
Command bus
Data bus
Row Acc
Col Acc
data
Command bus
Data bus
xRead
ADR
Resp bus
RDY
ID
Send
⓵
⓶
⓷
DRAM Operation
NVDIMM-P Operation
tRCD + tCAS (deterministic)
Mem Ctrl 0
Mem Ctrl 1
DDR5 DIMM
DDR5 DIMM
NVDIMM-P
NVDIMM-P
https://www.storagereview.com/node/7416
Mix DIMMs with different access timing on one memory channel
data
ID
⓸
Nondeterministic

## Slide 13: Outline
Introduction
Background
  DDR5 asynchronous memory operations
Network-attached DIMM
  NetDIMM hardware architecture
  NetDIMM software architecture
Evaluation
Conclusion

## Slide 14: NetDIMM Overall Architecture
CPU
Mem Ctrl 0
Mem Ctrl 1
DDR5 DIMM
DDR5 DIMM
NetDIMM
NetDIMM
DDR5 DIMM
DDR5 DIMM
Global/Shared Memory Channel

## Slide 15: NetDIMM Overall Architecture
CPU
Mem Ctrl 0
Mem Ctrl 1
DDR5 DIMM
DDR5 DIMM
NetDIMM
NetDIMM
DDR5 DIMM
DDR5 DIMM
DRAM
NetDIMM Buffer Device
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
Eth
Micron’s NVDIMM
FPGA Controller
DRAM Devices
Power
connector
Local Memory Channel
Buffered DIMM with an integrated NIC in a buffer device
DRAM devices
Buffer device + integrated NIC + other logic
Network
Connector
Global/Shared Memory Channel

## Slide 16: NetDIMM Overall Architecture
CPU
Mem Ctrl 0
Mem Ctrl 1
DDR5 DIMM
DDR5 DIMM
NetDIMM
NetDIMM
DDR5 DIMM
DDR5 DIMM
DRAM
NetDIMM Buffer Device
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
Eth
Local Memory Channel
CPU
DDR Memory
CPU
DDR Memory
CPU
DDR Memory
CPU
DDR Memory
CPU
DDR Memory
Micron’s NVDIMM
Global/Shared Memory Channel

## Slide 17: NetDIMM Overall Architecture
CPU
Mem Ctrl 0
Mem Ctrl 1
DDR5 DIMM
DDR5 DIMM
NetDIMM
NetDIMM
DDR5 DIMM
DDR5 DIMM
DRAM
NetDIMM Buffer Device
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
Eth
Local Memory Channel
Rack level memory disaggregation
CPU
DDR Memory
CPU
DDR Memory
CPU
DDR Memory
CPU
DDR Memory
CPU
DDR Memory
Micron’s NVDIMM
Global/Shared Memory Channel

## Slide 18: Higher Aggregate Memory Bandwidth with Commodity DRAM
Conventional memory system with PCIe network interface
  DMA RX/TX packets occupies global/shared memory channels
Memory Controller
DDR5 DIMM
DRAM
DRAM
Data Buffer
DDR5 DIMM
DRAM
DRAM
Data Buffer
Global/Shared Channel
NIC
RC
PCIe Link
Conventional Server Architecture

## Slide 19: Higher Aggregate Memory Bandwidth with Commodity DRAM
Conventional memory system with PCIe network interface
  DMA RX/TX packets occupies global/shared memory channels
  Interfere with processor memory accesses
Memory Controller
DDR5 DIMM
DRAM
DRAM
Data Buffer
DDR5 DIMM
DRAM
DRAM
Data Buffer
Global/Shared Channel
NIC
RC
PCIe Link
pkt
CPU
side
Conventional Server Architecture

## Slide 20: Higher Aggregate Memory Bandwidth with Commodity DRAM
Conventional memory system with near-memory network interface
  DMA RX/TX packets through local/private memory channels
Memory Controller
DDR5 DIMM
DRAM
DRAM
Data Buffer
Global/Shared Channel
RC
PCIe Link
NetDIMM
DRAM
DRAM
NetDIMM
Local/Private Channels
Memory Controller
DDR5 DIMM
DRAM
DRAM
Data Buffer
DDR5 DIMM
DRAM
DRAM
Data Buffer
Global/Shared Channel
NIC
RC
PCIe Link
Conventional Server Architecture
NetDIMM Server Architecture
Eth

## Slide 21: Higher Aggregate Memory Bandwidth with Commodity DRAM
Conventional memory system with near-memory network interface
  DMA RX/TX packets through local/private memory channels
Memory Controller
DDR5 DIMM
DRAM
DRAM
Data Buffer
Global/Shared Channel
RC
PCIe Link
NetDIMM
DRAM
DRAM
NetDIMM
Memory Controller
DDR5 DIMM
DRAM
DRAM
Data Buffer
DDR5 DIMM
DRAM
DRAM
Data Buffer
Global/Shared Channel
NIC
RC
PCIe Link
Conventional Server Architecture
NetDIMM Server Architecture
Eth
pkt
Local/Private Channels

## Slide 22: Higher Aggregate Memory Bandwidth with Commodity DRAM
Conventional memory system with near-memory network interface
  DMA RX/TX packets through local/private memory channels
  Higher aggregate system memory bandwidth
Memory Controller
DDR5 DIMM
DRAM
DRAM
Data Buffer
Global/Shared Channel
RC
PCIe Link
NetDIMM
DRAM
DRAM
NetDIMM
Memory Controller
DDR5 DIMM
DRAM
DRAM
Data Buffer
DDR5 DIMM
DRAM
DRAM
Data Buffer
Global/Shared Channel
NIC
RC
PCIe Link
Conventional Server Architecture
NetDIMM Server Architecture
Eth
pkt
pkt
CPU
side
Local/Private Channels

## Slide 23: Outline
Introduction
Background
  DDR5 asynchronous memory operations
Network-attached DIMM
  NetDIMM hardware architecture
  NetDIMM software architecture
Evaluation
Conclusion

## Slide 24: NetDIMM Hardware Architecture
DRAM
NetDIMM Buffer Device
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
DRAM
Eth
Local Mem Ctrl
nNIC
nPref
DRAM Devices
Global DDR
Channel
Near-Memory NIC
nCache
nController
DDR5 PHY
NetDIMM buffer device
Ethernet
Connector
Local/Private Channels

## Slide 25: NetDIMM Hardware Architecture
nController
  Datapath control for NIC/DDR5 PHY accesses
  Snoop write req and invalidate nCache
nCache
  Inclusive set-associative cache
  Invalidate after read
nPrefetcher
  Network data accesses are to consecutive addresses
  Start prefetching into nCache after the first access from host
Local Mem Ctrl
nNIC
nPref
DRAM Devices
Global DDR
Channel
Ethernet
Connector
NetDIMM buffer device
nCache
nController
DDR5 PHY
Local/Private Channels

## Slide 26: NetDIMM Hardware Architecture - Optimization
src and dest share a same sub array
  Fast Parallel Mode (FPM)
Otherwise
  Pipeline Serial Mode (PSM)
  General Cloning Mode (GCM)
*Accelerate copies in the network stack
Local Mem Ctrl
nNIC
nPref
DRAM Devices
Smart memory allocation needed to unleash the FPM benefits
Local/Private Channels
nCache
nController
DDR5 PHY
Global DDR
Channel
Ethernet
Connector
Row Buffer
dst
src
*RowClone-MICRO’13
NetDIMM buffer device

## Slide 27: Outline
Introduction
Background
  DDR5 asynchronous memory operations
Network-attached DIMM
  NetDIMM hardware architecture
  NetDIMM software architecture
Evaluation
Conclusion

## Slide 28: NetDIMM Software Architecture
Two components
NetDIMM memory management
  Physical memory mapping
  Memory allocation
NetDIMM driver
  Packet transmission and reception

## Slide 29: NetDIMM Memory Management
Physical memory mapping
  Flex-channel mode
    ✅ Channel level parallelism for regular accesses
    ✅ Network packets goes to the right channel
64GB
64GB
64GB
Host
CPU
Mem Ctrl 0
Mem Ctrl 1
DDR0
Net0
DDR1
64GB
Net1
0-64GB
64-128GB
128-192GB
192-256GB
256GB
Regular memory zone**
NetDIMM 0 zone*
NetDIMM 1 zone*
*Accessed using DDR5 asynchronous NIVDIMM-P operations
**Accessed using DDR5 regular DRAM operations

## Slide 30: NetDIMM Memory Management
Physical memory mapping
  Flex-channel mode
    ✅ Channel level parallelism for regular accesses
    ✅ Network packets goes to the right channel
Memory allocation
  Expose DRAM’s internal architecture to the memory scheduler
  __alloc_netdimm_pages(zone, hint)
  More details in the paper

## Slide 31: NetDIMM Packet Reception (RX)
@System bootup: allocate descriptor rings and DMA buffers
@driver – polling agent
  Check RX ring for new packets
RX at nNIC
  DMA data to rx ring
Memory Controller
NetDIMM #0
…
rx desc ring
DMA buffers
Global/Shared Channel
NetDIMM #1
DDR5 DIMM
nCache
DRAM
DDR
nNIC
CPU & Caches
Network SW Stack
Net0
Net1
HW
SW
Recv()
Send()
polling
pkt
NetDIMM Zones
Normal Zone
RX
TX
Reg Mem

## Slide 32: NetDIMM Packet Reception (RX)
@System bootup: allocate descriptor rings and DMA buffers
@driver – polling agent
  Check RX ring for new packets
RX at nNIC
  DMA data to rx ring
@driver RX engine
  allocate a skb on Net0 & invalidate skb
Network SW Stack
Net0
Net1
HW
SW
Recv()
Send()
polling
NetDIMM Zones
Normal Zone
RX
TX
Reg Mem
Memory Controller
NetDIMM #0
…
rx desc ring
DMA buffers
Global/Shared Channel
NetDIMM #1
DDR5 DIMM
nCache
DRAM
DDR
nNIC
CPU & Caches
pkt

## Slide 33: NetDIMM Packet Reception (RX)
@System bootup: allocate descriptor rings and DMA buffers
@driver – polling agent
  Check RX ring for new packets
RX at nNIC
  DMA data to rx ring
@driver RX engine
  allocate a skb on Net0 & invalidate skb
  In-DRAM copy to skb
  Send skb ptr to network stack
@network stack/above
  Next line prefetch into nCache
Network SW Stack
Net0
Net1
HW
SW
Recv()
Send()
polling
NetDIMM Zones
Normal Zone
RX
TX
Reg Mem
Memory Controller
NetDIMM #0
…
rx desc ring
DMA buffers
Global/Shared Channel
NetDIMM #1
DDR5 DIMM
nCache
DRAM
DDR
nNIC
CPU & Caches
$
$
$
$
$
pkt
nCache improves NetDIMM access latency
pkt
pkt
pkt
pkt

## Slide 34: Experimental Methodology
gem5 full-system simulation
  Linux and baremetal drivers
  Remove kernel software stack overhead
Facebook traces from three different clusters
Chart: Packet Size (Bytes)
| 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700 | 800 | 900 | 1000 | 1100 | 1200 | 1300 | 1400 | 1500 | 1600
database | 0 | 0.27066 | 0.38301 | 0.43294 | 0.50877 | 0.56027 | 0.64046 | 0.68989 | 0.73574 | 0.76303 | 0.79963 | 0.81835 | 0.83774 | 0.85048 | 0.8652 | 0.87593 | 1
webserver | 0 | 0.40462 | 0.68136 | 0.88258 | 0.92705 | 0.94137 | 0.94917 | 0.95593 | 0.95931 | 0.96148 | 0.96526 | 0.96743 | 0.9692 | 0.97258 | 0.97402 | 0.97531 | 1
hadoop | 0 | 0.39852 | 0.41515 | 0.41779 | 0.42724 | 0.43645 | 0.4383 | 0.43985 | 0.442 | 0.4451 | 0.44691 | 0.44867 | 0.45072 | 0.45322 | 0.47441 | 0.4757 | 1
Parameters | Values
Cores/freq | 8 / 3.4GHz/ 3ways
superscalar | 3 ways
Caches (size, assoc) I/D/L2 | 32KB, 2/64KB, 2/2MB,16ways
DRAM | DDR4-2400/2Channels
Network/#NetDIMMs | 40Gbps/1
PCIe | X8 PCIe 4
Configuration | Description
PCIe NIC | Discrete PCIe NIC
Intg NIC | Integrated NIC into CPU
ND Base | NetDIMM w/o RowClone
ND RowC | NetDIMM w/ RowClone

## Slide 35: Experimental Results – Total Network Latency
Chart: Packet Size
| ND Base | ND RowC | Intg NIC | PCIe NIC | ND Base | ND RowC | Intg NIC | PCIe NIC | ND Base | ND RowC | Intg NIC | PCIe NIC | 64 Bytes | 512 Bytes | 2048 Bytes
total | 0.5936 | 0.53878 | 0.61671 | 1 | 0.76763 | 0.65291 | 0.90293 | 1.3142 | 1.08 | 0.89393 | 1.3023 | 1.8131
NetDIMM without RowClone
NetDIMM with RowClone

## Slide 36: Experimental Results – Total Network Latency
Vs. PCIe NIC
  Up to 50.7%
Chart: Packet Size
| ND Base | ND RowC | Intg NIC | PCIe NIC | ND Base | ND RowC | Intg NIC | PCIe NIC | ND Base | ND RowC | Intg NIC | PCIe NIC | 64 Bytes | 512 Bytes | 2048 Bytes
total | 0.5936 | 0.53878 | 0.61671 | 1 | 0.76763 | 0.65291 | 0.90293 | 1.3142 | 1.08 | 0.89393 | 1.3023 | 1.8131
50.7%
50.3%
46.1%
40.6%
41.5%
40.4%

## Slide 37: Experimental Results – Total Network Latency
Vs. PCIe NIC
  Up to 50.7%
Vs. intg NIC
  Up to 31.4%
Chart: Packet Size
| ND Base | ND RowC | Intg NIC | PCIe NIC | ND Base | ND RowC | Intg NIC | PCIe NIC | ND Base | ND RowC | Intg NIC | PCIe NIC | 64 Bytes | 512 Bytes | 2048 Bytes
total | 0.5936 | 0.53878 | 0.61671 | 1 | 0.76763 | 0.65291 | 0.90293 | 1.3142 | 1.08 | 0.89393 | 1.3023 | 1.8131
31.4%
27.7%
12.6%
3.7%
14.9%
17.1%

## Slide 38: Experimental Results – Network Latency Breakdown
Chart: Normalized Network Latency
| ND Base | ND RowC | Intg NIC | PCIe NIC
wire | 0.072234 | 0.072234 | 0.072234 | 0.072234
DMA | 0.14252 | 0.14252 | 0.14868 | 0.34719
I/O reg acc | 0.19803 | 0.19803 | 0.16317 | 0.27152
copy | 0.11638 | 0.029096 | 0.30905 | 0.30905
flush/inv | 0.054933 | 0.054933 | 0 | 0
2048 Bytes packet size

## Slide 39: Experimental Results – Network Latency Breakdown
2048 Bytes packet size
Buffer copying improvements vs. PCIe:
  ND Base: 62.3% lower
  ND RowC: 90.5% lower
Chart: Normalized Network Latency
| ND Base | ND RowC | Intg NIC | PCIe NIC
wire | 0.072234 | 0.072234 | 0.072234 | 0.072234
DMA | 0.14252 | 0.14252 | 0.14868 | 0.34719
I/O reg acc | 0.19803 | 0.19803 | 0.16317 | 0.27152
copy | 0.11638 | 0.029096 | 0.30905 | 0.30905
flush/inv | 0.054933 | 0.054933 | 0 | 0

## Slide 40: Experimental Results – Network Latency Breakdown
2048 Bytes packet size
Buffer copying improvements vs. PCIe:
  ND Base: 62.3% lower
  ND RowC: 90.5% lower
Rx and Tx DMA vs. PCIe
  ND Base and RowC: 59.0% lower
Chart: Normalized Network Latency
| ND Base | ND RowC | Intg NIC | PCIe NIC
wire | 0.072234 | 0.072234 | 0.072234 | 0.072234
DMA | 0.14252 | 0.14252 | 0.13068 | 0.34719
I/O reg acc | 0.19803 | 0.19803 | 0.16317 | 0.27152
copy | 0.11638 | 0.029096 | 0.30905 | 0.30905
flush/inv | 0.054933 | 0.054933 | 0 | 0

## Slide 41: Cluster-Level Avg and 99th percentile Network Latency
↑ switch latency == ↓ latency gain
Chart: Network Switch Latency
| 25ns | 100ns | 25ns | 100ns | average | 99th
database | 0.59237 | 0.70797 | 0.4442 | 0.62478
webserver | 0.5569 | 0.64469 | 0.33464 | 0.51992
hadoop | 0.63567 | 0.70704 | 0.56158 | 0.66545

## Slide 42: Cluster-Level Avg and 99th percentile Network Latency
↑ switch latency == ↓ latency gain
Hadoop:
  Lowest improvement among other clusters:
  Avg: 29% ~ 36%
  99th: 33% ~ 44%
Chart: Network Switch Latency
| 25ns | 100ns | 25ns | 100ns | average | 99th
database | 0.59237 | 0.70797 | 0.4442 | 0.62478
webserver | 0.5569 | 0.64469 | 0.33464 | 0.51992
hadoop | 0.63567 | 0.70704 | 0.56158 | 0.66545

## Slide 43: Cluster-Level Avg and 99th percentile Network Latency
↑ switch latency == ↓ latency gain
Hadoop:
  Lowest improvement among other clusters:
  Avg: 29% ~ 36%
  99th: 33% ~ 44%
Webserver:
  Highest improvement among other clusters
  Avg: 36% ~ 44%
  99th: 48% ~ 67%
Chart: Network Switch Latency
| 25ns | 100ns | 25ns | 100ns | average | 99th
database | 0.59237 | 0.70797 | 0.4442 | 0.62478
webserver | 0.5569 | 0.64469 | 0.33464 | 0.51992
hadoop | 0.63567 | 0.70704 | 0.56158 | 0.66545

## Slide 44: Conclusion
Need to rethink network architecture to optimize it for Latency and Bandwidth together
NetDIMM: Near-memory network interface architecture
  DDR5 asynch support for unified memory
  Leverage network data access pattern by prefetching and caching
  In-memory buffer cloning to reduce network stack data copying
Latency improvement without compromising bandwidth
  Up to 50.7% and 30.9% compared with PCIe and Integrated NICs
Opens an avenue for software define memory and composable architectures

## Slide 45: Questions?