## Slide 1: Simulating PCI-Express Interconnect for Future System Exploration
Mohammad Alian, Krishna Parasuram Sirinivasan, Nam Sung Kim
University of Illinois Urbana-Champaign

## Slide 2: Motivation
PCIe is the dominant I/O interconnection technology
  Network Interface Card
  GPU
  SSD
  Accelerators
  Memory Drive Technology
  Emerging rack-scale systems

## Slide 3: PCIe Use Case: Memory Drive Technology
Use Intel Optane SSD as Main Mem
Intel

## Slide 4: PCIe Use Case: Rack Scale Design
Compute, memory, storage, accelerators and network pool
PCIe Gen4

## Slide 5: PCIe Use Case: Rack Scale Design
Compute, memory, storage, accelerators and network pool
M. Jung et al. “SimpleSSD: Modeling Solid State Drives for Holistic System Simulation,” CAL’17
N. Binkert et al. “The gem5 simulator,” ACM SIGARCH 2011
A. Hansson et al. “Simulating DRAM controllers for future system architecture exploration,” ISPASS 2014
M. Alian et al. “dist-gem5: Distributed Simulation of Computer Clusters,” ISPASS 2017
J. Power et al. “gem5-gpu: A Heterogeneous CPU-GPU Simulator,“ CAL 2015
PCIe Gen4

## Slide 6: gem5 Off-chip Interconnection Model
Architectural simulators ignore I/O performance modeling
gem5 has a simple functional crossbar model for the I/O interconnection
  Loosely model a PCI bus
  Does not model the complex PCIe protocol
In this work we build a PCIe model for gem5
gem5 IO architecture
Slave port
Master port

## Slide 7: Outline
Motivation
Background
  PCI vs. PCIe architecture
PCI-Express Modeling
  Enabling functionality (Detect a PCIe device)
  Performance modeling for root complex, switch, and links
Evaluation
Conclusion

## Slide 8: Background: PCI Bus
Parallel bus
  33MHz (133 MB/sec) or 66MHz (533 MB/sec)
PCI Bridges form a hierarchy
Each bus supports up to 12 electrical loads
  bridges and endpoints
  4 shared interrupt lines
Does not support split transaction
Endpoint
PCI-PCI
Bridge
Host-PCI
Bridge
Endpoint
PCI-PCI
Bridge
….
….
….
Endpoint
Endpoint
Processor and Memory

## Slide 9: Background: PCIe Interconnection
Dual point to point serial connection
  x1, x2, x4, x8, x12, x16, x32
  Packet based protocol
  1GB/sec transfer rate for PCIe 3.0
  Split transactions
Each endpoint can work at a different speed
8b/10b and 128b/130b encoding
MSI/MSI-X interrupt handling
  Also supports legacy PCI interrupts
Additional capabilities
  Power management, error reporting, etc.
"PCI Express Basics". PCI-SIG.
…
Device A
Device B
Lane
Link
Wire
Packet

## Slide 10: Background: PCIe Interconnection (cont.)
Layered architecture
  Transaction, Data Link, and Physical
Transaction Layer Packet (TLP) types
  Memory read/write
  I/O read/write
  Configuration read/write
  Messages
    Used for events like MSI
Transaction layer
Data link layer
Physical layer
Device
to/from physical layer
of another device
start
seq
header
payload
ECRC
LCRC
end
Data link layer packet
Transaction layer packet
Physical layer packet

## Slide 11: Our Approach to Enable PCIe in gem5
Take a PCI device model as a base and enable it to work with PCI Express driver
  Define necessary configuration space registers and data structures
  Enable the driver to read/write from/to the configuration space
  Set read-only configuration registers
Implement root complex and PCIe switch models
  Create a functional model that represents PCIe hierarchy
Implement timing models for PCIe link and switches
  Configurable latency and bandwidth
  ACK/NAK protocol
Enable functionality
Add performance modeling

## Slide 12: Our Approach to Enable PCIe in gem5
Take a PCI device model as a base and enable it to work with PCI Express driver
  Define necessary configuration space registers and data structures
  Enable the driver to read/write from/to the configuration space
  Set read-only configuration registers
Implement root complex and PCIe switch models
  Create a model that represents PCIe hierarchy
Implement a PCIe link model
  Configurable latency and bandwidth
  ACK/NAK protocol

## Slide 13: Our Approach to Enable PCIe in gem5
Take a PCI device model as a base and enable it to work with PCI Express driver
  Define necessary configuration space registers and data structures
  Enable the driver to read/write from/to the configuration space
  Set read-only configuration registers
Implement root complex and PCIe switch models
  Create a model that represents PCIe hierarchy
Implement a PCIe link model
  Configurable latency and bandwidth
  ACK/NAK protocol

## Slide 14: PCI-Express Endpoint Configuration Header
Endpoint Configuration Header
256Bytes
PCI and PCIe
PCIe only
Used to match a device with a device driver

## Slide 15: Virtual P2P Bridge Configuration Header

## Slide 16: PCIe Enumeration
During system boot up
Detect active PCIe devices
Initialize their Base Address Register (BAR)
Uses Bus:Device:Function (BDF) addressing
  00:02.0 => bus 0, device 2, function 0

## Slide 17: PCIe Enumeration
Host Bridge
Root Complex
Switch
P2P
P2P
P2P
P2P
P2P
P2P
P2P
endpoint
endpoint

## Slide 18: PCIe Enumeration
Before PCIe Enumeration
  Assuming single function devices (function number is 0 for all devices)
Enumeration sets:
  Bus number
  Secondary bus number (sec)
    Minimum bus number in the tree
  Subordinate bus number (sub)
    Maximum bus number in the tree
Host Bridge
Root Complex
Switch
dev 0
sec
sub
dev 1
sec
sub
dev 2
sec
sub
dev 0
sec
sub
dev 1
sec
sub
dev 2
sec
sub
dev 0
sec
sub
dev 0
dev 0

## Slide 19: PCIe Enumeration
Before PCIe Enumeration
  Assuming single function devices (function number is 0 for all devices)
Enumeration sets:
  Bus number
  Secondary bus number (sec)
    Minimum bus number in the tree
  Subordinate bus number (sub)
    Maximum bus number in the tree
Host Bridge
Root Complex
Switch
dev 0
sec
sub
dev 1
sec
sub
dev 2
sec
sub
dev 0
sec
sub
dev 1
sec
sub
dev 2
sec
sub
dev 0
sec
sub
dev 0
dev 0
bus 0

## Slide 20: PCIe Enumeration
Before PCIe Enumeration
  Assuming single function devices (function number is 0 for all devices)
Enumeration sets:
  Bus number
  Secondary bus number (sec)
    Minimum bus number in the tree
  Subordinate bus number (sub)
    Maximum bus number in the tree
Host Bridge
Root Complex
Switch
dev 0
sec 1
sub 255
dev 1
sec
sub
dev 2
sec
sub
dev 0
sec
sub
dev 1
sec
sub
dev 2
sec
sub
dev 0
sec
sub
dev 0
dev 0
bus 0
bus 1

## Slide 21: PCIe Enumeration
Before PCIe Enumeration
  Assuming single function devices (function number is 0 for all devices)
Enumeration sets:
  Bus number
  Secondary bus number (sec)
    Minimum bus number in the tree
  Subordinate bus number (sub)
    Maximum bus number in the tree
Host Bridge
Root Complex
Switch
dev 0
sec 1
sub 255
dev 1
sec
sub
dev 2
sec
sub
dev 0
sec
sub
dev 1
sec
sub
dev 2
sec
sub
dev 0
sec 2
sub 255
dev 0
dev 0
bus 0
bus 1
bus 2

## Slide 22: PCIe Enumeration
Before PCIe Enumeration
  Assuming single function devices (function number is 0 for all devices)
Enumeration sets:
  Bus number
  Secondary bus number (sec)
    Minimum bus number in the tree
  Subordinate bus number (sub)
    Maximum bus number in the tree
Host Bridge
Root Complex
Switch
dev 0
sec 1
sub 255
dev 1
sec
sub
dev 2
sec
sub
dev 0
sec 3
sub 255
dev 1
sec
sub
dev 2
sec
sub
dev 0
sec 2
sub 255
dev 0
dev 0
bus 0
bus 1
bus 2
bus 3

## Slide 23: PCIe Enumeration
Before PCIe Enumeration
  Assuming single function devices (function number is 0 for all devices)
Enumeration sets:
  Bus number
  Secondary bus number (sec)
    Minimum bus number in the tree
  Subordinate bus number (sub)
    Maximum bus number in the tree
Host Bridge
Root Complex
Switch
dev 0
sec 1
sub 255
dev 1
sec
sub
dev 2
sec
sub
dev 0
sec 3
sub 3
dev 1
sec
sub
dev 2
sec
sub
dev 0
sec 2
sub 255
dev 0
dev 0
bus 0
bus 1
bus 2
bus 3

## Slide 24: PCIe Enumeration
Before PCIe Enumeration
  Assuming single function devices (function number is 0 for all devices)
Enumeration sets:
  Bus number
  Secondary bus number (sec)
    Minimum bus number in the tree
  Subordinate bus number (sub)
    Maximum bus number in the tree
Host Bridge
Root Complex
Switch
dev 0
sec 1
sub 255
dev 1
sec
sub
dev 2
sec
sub
dev 0
sec 3
sub 3
dev 1
sec 255
sub 0
dev 2
sec
sub
dev 0
sec 2
sub 255
dev 0
dev 0
bus 0
bus 1
bus 2
bus 3

## Slide 25: PCIe Enumeration
Before PCIe Enumeration
  Assuming single function devices (function number is 0 for all devices)
Enumeration sets:
  Bus number
  Secondary bus number (sec)
    Minimum bus number in the tree
  Subordinate bus number (sub)
    Maximum bus number in the tree
Host Bridge
Root Complex
Switch
dev 0
sec 1
sub 255
dev 1
sec
sub
dev 2
sec
sub
dev 0
sec 3
sub 3
dev 1
sec 255
sub 0
dev 2
sec 255
sub 0
dev 0
sec 2
sub 255
dev 0
dev 0
bus 0
bus 1
bus 2
bus 3

## Slide 26: PCIe Enumeration
Before PCIe Enumeration
  Assuming single function devices (function number is 0 for all devices)
Enumeration sets:
  Bus number
  Secondary bus number (sec)
    Minimum bus number in the tree
  Subordinate bus number (sub)
    Maximum bus number in the tree
Host Bridge
Root Complex
Switch
dev 0
sec 1
sub 255
dev 1
sec
sub
dev 2
sec
sub
dev 0
sec 3
sub 3
dev 1
sec 255
sub 0
dev 2
sec 255
sub 0
dev 0
sec 2
sub 3
dev 0
dev 0
bus 0
bus 1
bus 2
bus 3

## Slide 27: PCIe Enumeration
Before PCIe Enumeration
  Assuming single function devices (function number is 0 for all devices)
Enumeration sets:
  Bus number
  Secondary bus number (sec)
    Minimum bus number in the tree
  Subordinate bus number (sub)
    Maximum bus number in the tree
Host Bridge
Root Complex
Switch
dev 0
sec 1
sub 3
dev 1
sec
sub
dev 2
sec
sub
dev 0
sec 3
sub 3
dev 1
sec 255
sub 0
dev 2
sec 255
sub 0
dev 0
sec 2
sub 3
dev 0
dev 0
bus 0
bus 1
bus 2
bus 3

## Slide 28: PCIe Enumeration
Before PCIe Enumeration
  Assuming single function devices (function number is 0 for all devices)
Enumeration sets:
  Bus number
  Secondary bus number (sec)
    Minimum bus number in the tree
  Subordinate bus number (sub)
    Maximum bus number in the tree
Host Bridge
Root Complex
Switch
dev 0
sec 1
sub 3
dev 1
sec 255
sub 0
dev 2
sec 4
sub 4
dev 0
sec 3
sub 3
dev 1
sec 255
sub 0
dev 2
sec 255
sub 0
dev 0
sec 2
sub 3
dev 0
dev 0
bus 0
bus 1
bus 2
bus 3
bus 4

## Slide 29: PCIe Enumeration
Before PCIe Enumeration
  Assuming single function devices (function number is 0 for all devices)
Enumeration sets:
  Bus number
  Secondary bus number (sec)
    Minimum bus number in the tree
  Subordinate bus number (sub)
    Maximum bus number in the tree
Initialize BAR using BDF addressing
  assign IO and memory space
Host Bridge
Root Complex
Switch
dev 0
sec 1
sub 3
dev 1
sec 255
sub 0
dev 2
sec 4
sub 4
dev 0
sec 3
sub 3
dev 1
sec 255
sub 0
dev 2
sec 255
sub 0
dev 0
sec 2
sub 3
dev 0
dev 0
bus 0
bus 1
bus 2
bus 3
bus 4

## Slide 30: Our Approach to Enable PCIe in gem5
Take a PCI device model as a base and enable it to work with PCI Express driver
  Define necessary configuration space registers and data structures
  Enable the driver to read/write from/to the configuration space
  Set read-only configuration registers
Implement root complex and PCIe switch models
  Create a model that represents PCIe hierarchy
Implement a PCIe link model
  Configurable latency and bandwidth
  ACK/NAK protocol

## Slide 31: Root Complex Model
Master port (M)
  Request
Slave ports (S)
  response
Root complex is connected to the Mem Bus
  Used an IO cache for DMA transaction to enforce coherency
P2P bridges perform packet routing
  based on I/O and memory address space
Configurable latency and bandwidth
endpoint
Switch
M
P2P
P2P
P2P
IOCache
S
M
S
M
Internal Bus 0
Root Complex
S
Root Port 1
Root Port 2
Root Port 3
S
M
M
S
S
M
M
S
S
M
M
S
endpoint
Memory Bus
LLC
Memory Ctrl
PIO Requests
DMA Requests

## Slide 32: Our Approach to Enable PCIe in gem5
Take a PCI device model as a base and enable it to work with PCI Express driver
  Define necessary configuration space registers and data structures
  Enable the driver to read/write from/to the configuration space
  Set read-only configuration registers
Implement root complex and PCIe switch models
  Create a model that represents PCIe hierarchy
Implement a PCIe link model
  Configurable latency and bandwidth
  ACK/NAK protocol

## Slide 33: PCIe Link Model
Consists of two unidirectional links
Configurable latency and bandwidth
  model different lane width/generation
Add overhead of protocol layers
RX Logic
TX Logic
TX Logic
RX Logic
S
pcie-pkt
pcie-pkt
M
M
S
S
M
Root Complex/Switch
Downstream Port
Endpoint/Switch Upstream Port
M
S

## Slide 34: PCIe Link Model
RX Logic
TX Logic
TX Logic
RX Logic
S
pcie-pkt
pcie-pkt
M
M
S
S
M
Root Complex/Switch
Downstream Port
Endpoint/Switch Upstream Port
M
S

## Slide 35: PCIe Link Model
TX Logic
TX Logic
RX Logic
S
pcie-pkt
pcie-pkt
M
M
S
S
M
Root Complex/Switch
Downstream Port
Endpoint/Switch Upstream Port
M
S
RX Logic

## Slide 36: PCIe Link Model
is
ack
Seq Check
S
Seq Gen
S0
Reply buffer
Reply Timer
MUX
M
Ack Timer
Reply Timer
Reply buffer
Dequeue
NO
YES
packet
S0
S1
S1
TX Logic
TX Logic
RX Logic
S
pcie-pkt
pcie-pkt
M
M
S
S
M
Root Complex/Switch
Downstream Port
Endpoint/Switch Upstream Port
M
S
RX Logic
is
ack
Notes: Reply timer starts from 0 when the last byte of any TLP is sent. It restarts when a new TLP is sent or when an ACK DLLP is received that references a packet in the replay buffer.

## Slide 37: PCIe Link Model
S
Seq Gen
Reply buffer
Reply Timer
M
TX Logic
TX Logic
RX Logic
S
pcie-pkt
pcie-pkt
M
M
S
S
M
Root Complex/Switch
Downstream Port
Endpoint/Switch Upstream Port
M
S
RX Logic
seq
check
seq
check
Next Seq
Ack/NAC Gen
Timer
OK
Notes: Reply timer starts from 0 when the last byte of any TLP is sent. It restarts when a new TLP is sent or when an ACK DLLP is received that references a packet in the replay buffer.

## Slide 38: PCIe Link Model
S
Seq Gen
Reply buffer
Reply Timer
M
packet
TX Logic
TX Logic
RX Logic
S
pcie-pkt
pcie-pkt
M
M
S
S
M
Root Complex/Switch
Downstream Port
Endpoint/Switch Upstream Port
M
S
RX Logic
seq
check
seq
check
Next Seq
Ack/NAC Gen
Timer
OK
0
Notes: Reply timer starts from 0 when the last byte of any TLP is sent. It restarts when a new TLP is sent or when an ACK DLLP is received that references a packet in the replay buffer.

## Slide 39: PCIe Link Model
S
Seq Gen
Reply buffer
Reply Timer
M
packet
TX Logic
TX Logic
RX Logic
S
pcie-pkt
pcie-pkt
M
M
S
S
M
Root Complex/Switch
Downstream Port
Endpoint/Switch Upstream Port
M
S
RX Logic
seq
check
seq
check
Next Seq
Ack/NAC Gen
Timer
OK
0
Notes: Reply timer starts from 0 when the last byte of any TLP is sent. It restarts when a new TLP is sent or when an ACK DLLP is received that references a packet in the replay buffer.

## Slide 40: PCIe Link Model
S
Seq Gen
Reply buffer
Reply Timer
M
packet
TX Logic
TX Logic
RX Logic
S
pcie-pkt
pcie-pkt
M
M
S
S
M
Root Complex/Switch
Downstream Port
Endpoint/Switch Upstream Port
M
S
RX Logic
seq
check
seq
check
Next Seq
Ack/NAC Gen
Timer
OK
0
Notes: Reply timer starts from 0 when the last byte of any TLP is sent. It restarts when a new TLP is sent or when an ACK DLLP is received that references a packet in the replay buffer.

## Slide 41: PCIe Link Model
S
Seq Gen
Reply buffer
Reply Timer
M
packet
TX Logic
TX Logic
RX Logic
S
pcie-pkt
pcie-pkt
M
M
S
S
M
Root Complex/Switch
Downstream Port
Endpoint/Switch Upstream Port
M
S
RX Logic
seq
check
seq
check
Next Seq
Ack/NAC Gen
Timer
OK
S0
0
Notes: Reply timer starts from 0 when the last byte of any TLP is sent. It restarts when a new TLP is sent or when an ACK DLLP is received that references a packet in the replay buffer.

## Slide 42: PCIe Link Model
S
Seq Gen
Reply buffer
Reply Timer
M
packet
TX Logic
TX Logic
RX Logic
S
pcie-pkt
pcie-pkt
M
M
S
S
M
Root Complex/Switch
Downstream Port
Endpoint/Switch Upstream Port
M
S
RX Logic
seq
check
seq
check
Next Seq
Ack/NAC Gen
Timer
OK
S1
0
Notes: Reply timer starts from 0 when the last byte of any TLP is sent. It restarts when a new TLP is sent or when an ACK DLLP is received that references a packet in the replay buffer.

## Slide 43: PCIe Link Model
S
Seq Gen
Reply buffer
Reply Timer
M
packet
TX Logic
TX Logic
RX Logic
S
pcie-pkt
pcie-pkt
M
M
S
S
M
Root Complex/Switch
Downstream Port
Endpoint/Switch Upstream Port
M
S
RX Logic
seq
check
seq
check
Next Seq
Ack/NAC Gen
Timer
OK
S0
1
Notes: Reply timer starts from 0 when the last byte of any TLP is sent. It restarts when a new TLP is sent or when an ACK DLLP is received that references a packet in the replay buffer.

## Slide 44: PCIe Link Model
S
Seq Gen
Reply buffer
Reply Timer
M
packet
TX Logic
TX Logic
RX Logic
S
pcie-pkt
pcie-pkt
M
M
S
S
M
Root Complex/Switch
Downstream Port
Endpoint/Switch Upstream Port
M
S
RX Logic
seq
check
seq
check
Next Seq
Ack/NAC Gen
Timer
OK
S1
1
Notes: Reply timer starts from 0 when the last byte of any TLP is sent. It restarts when a new TLP is sent or when an ACK DLLP is received that references a packet in the replay buffer.

## Slide 45: PCIe Link Model
S
Seq Gen
Reply buffer
Reply Timer
M
packet
TX Logic
TX Logic
RX Logic
S
pcie-pkt
pcie-pkt
M
M
S
S
M
Root Complex/Switch
Downstream Port
Endpoint/Switch Upstream Port
M
S
RX Logic
seq
check
seq
check
Next Seq
Ack/NAC Gen
Timer
OK
S1
1
Notes: Reply timer starts from 0 when the last byte of any TLP is sent. It restarts when a new TLP is sent or when an ACK DLLP is received that references a packet in the replay buffer.

## Slide 46: PCIe Link Model
S
Seq Gen
Reply buffer
Reply Timer
M
packet
TX Logic
TX Logic
RX Logic
S
pcie-pkt
pcie-pkt
M
M
S
S
M
Root Complex/Switch
Downstream Port
Endpoint/Switch Upstream Port
M
S
RX Logic
seq
check
seq
check
Next Seq
Ack/NAC Gen
Timer
OK
S1
S0
1
Notes: Reply timer starts from 0 when the last byte of any TLP is sent. It restarts when a new TLP is sent or when an ACK DLLP is received that references a packet in the replay buffer.

## Slide 47: PCIe Link Model
S
Seq Gen
Reply buffer
Reply Timer
M
packet
TX Logic
TX Logic
RX Logic
S
pcie-pkt
pcie-pkt
M
M
S
S
M
Root Complex/Switch
Downstream Port
Endpoint/Switch Upstream Port
M
S
RX Logic
seq
check
seq
check
Next Seq
Ack/NAC Gen
Timer
OK
S1
S0
1
Notes: Reply timer starts from 0 when the last byte of any TLP is sent. It restarts when a new TLP is sent or when an ACK DLLP is received that references a packet in the replay buffer.

## Slide 48: PCIe Link Model
S
Seq Gen
Reply buffer
Reply Timer
M
packet
TX Logic
TX Logic
RX Logic
S
pcie-pkt
pcie-pkt
M
M
S
S
M
Root Complex/Switch
Downstream Port
Endpoint/Switch Upstream Port
M
S
RX Logic
seq
check
seq
check
Next Seq
Ack/NAC Gen
Timer
OK
S0
1
Notes: Reply timer starts from 0 when the last byte of any TLP is sent. It restarts when a new TLP is sent or when an ACK DLLP is received that references a packet in the replay buffer.

## Slide 49: PCIe Link Model
S
Seq Gen
Reply buffer
Reply Timer
M
packet
TX Logic
TX Logic
RX Logic
S
pcie-pkt
pcie-pkt
M
M
S
S
M
Root Complex/Switch
Downstream Port
Endpoint/Switch Upstream Port
M
S
RX Logic
seq
check
seq
check
Next Seq
Ack/NAC Gen
Timer
OK
1
Notes: Reply timer starts from 0 when the last byte of any TLP is sent. It restarts when a new TLP is sent or when an ACK DLLP is received that references a packet in the replay buffer.

## Slide 50: Methodology
Physical setup
Xeon V4 E5 2660 processor, Intel p3700 SSD
Run “dd” to flood storage device with read/write requests
gem5 setup
Configure it to model the Xeon processor
IDE disk model does not impose any bandwidth bottleneck

## Slide 51: Validation
gem5 Setup
Root Complex
Switch
IDE Disk
Physical Setup
PCIe gen2 x4
PCIe gen2 x1
~5Gbps

## Slide 52: Validation
Different switch latency and access block size
  Within 80% ~ 90% of physical bandwidth
Chart: Block Size (MB)
| 64 | 128 | 256 | 512
phys | 2.864 | 2.88 | 3.096 | 3.2
L150ns | 2.544 | 2.568 | 2.592 | 2.592
L100ns | 2.568 | 2.608 | 2.632 | 2.632
L75ns | 2.592 | 2.632 | 2.648 | 2.656
L50ns | 2.616 | 2.648 | 2.672 | 2.68
Switch latency

## Slide 53: Bandwidth vs. Lane Width
BW drop from x4 to x8!
Switch port becomes the bottleneck
  Frequent replays – 27% of pkts
Chart: Block Size (MB)
| 64 | 128 | 256 | 512
x1 | 2.48 | 2.504 | 2.52 | 2.528
x2 | 4.056 | 4.16 | 4.208 | 4.224
x4 | 4.968 | 5.008 | 5.016 | 5.016
x8 | 4.584 | 4.72 | 4.768 | 4.792
Nonintuitive behavior which cannot be captured with a simple interconnection model

## Slide 54: Conclusion

## Slide 55: Backup slides